## Slide 1: Introduction to Next-Generation Sequencing
CITI Genomics workshop

## Slide 2: Outline
What is next-generation sequencing, and how is it used?
How do you construct a sequencing library?
Sequencing-by-Synthesis: what a sequencing machine is really doing
Raw data format: Fastq files
Pipeline overview
  File formats
  Important parameters to consider
Read Mapping: SAM files
SNP Calling: VCF files

## Slide 3: What is “Next-Gen” Sequencing (NGS)?
  The term “next-gen” can be applied to numerous modern sequencing methods; the key criteria common to all NGS methods are:
    High Throughput/ ”Massively” parallel
    DNA synthesis and detection happen at the same time (sequencing-by-synthesis)
    Low cost per base pair
  NGS methods are distinct from what is called Sanger sequencing (the traditional, low-throughput method)
  Commonly used NGS technologies:
    Illumina
    454 (Roche)
    Ion Torrent
    SOLiD
    Nanopore
    PacBio SMRT sequencing

## Slide 4: NGS Methods and Their Applications
Platform | Chemistry | Read Length | Run Time | Total Gb/Run | Pros | Cons | Typical Uses
 | Reversible Terminator | ~100bp | 5 days | 200 Gb | Low cost per run High throughput Most commonly used | Short reads Long run times | Everything (DNA, RNA, CHiP, Micro-biome, etc.)
 | Pyro-sequencing | ~700bp | 1 day | 0.7 Gb | Long reads Commonly used | Lower total bases Higher cost | Microbiome, Amplicons, Exomes
 | Pyro-sequencing | ~100bp | 8 days | 60 Gb | Low error rate | Short reads Long run times | CHiP Seq Methylation sequencing
 | Proton detection | ~200bp | 2 hrs | 100 Gb | Short run time Affordable equipment | Shorter reads Fewer users | Clinical labs Microbiome Targeted seq
 | Electric Current Density | >10,000bp | 2 hrs | 10 Gb | Short run time No PCR step Long reads | Higher cost/read High error rates Biased errors | Repeated sequencing (monitoring) Field tests
 | Real-time single molecule sequencing | >10,000bp | 30 min. | 2 Gb | Short run time Longest reads No PCR step | Higher cost/read High error rate (but random errors) | Whole genome assemblies Resequencing

## Slide 5: Whole Genome Sequencing (WGS)
  Original, and still most common application of NGS
  Most often used for Resequencing: sequencing an individual from a species that already has a publicly available reference genome
  The purpose of resequencing is to find small scale variations among individuals
    Mutations in the DNA: single base substitution, small deletions or small insertions
    Typically referred to as SNPs (Single Nucleotide Polymorphisms)
  SNP data is useful for many types of biological studies:
    Medical: finding mutations that cause diseases, or markers that indicate a risk for disease
    DNA fingerprinting: identifying individuals and testing relatedness (forensics)
    Phylogenomics (finding evolutionary relationships among individuals or species)
    Population genetics: testing for loci under natural selection, etc.
    Agriculture: testing purity of seed stocks; using markers to select lines for breeding
    And more!

## Slide 6: Constructing an Illumina Library
Start with genomic DNA:
Randomly fragment DNA:
(usually with sonication)
Add Forward and Reverse Adapters:
PCR amplification:
Size Selection:
~500 bp
Final Library:
Flowcell Binding Site
Forward Primer Site
Overhang
Reverse Primer Site
Overhang

## Slide 7: Sequencing-By-Synthesis
Library:
Illumina Flow Cell w/ 8 lanes
Flow cell is pre-coated with small DNA oligos
Fragments in the library are bound to the oligos on the flow cell (via the recognition seq. on the ends of the adapters)
A
T
A
C
T
G
A
T
A
C
T
G
A
T
A
G
T
G
Cross section of one cluster (notice there is a mutation/PCR error at one position)
A
C
G
T
Add labeled nucleotides
In situ amplification creates clusters of identical copies of each fragment
T
T
T
Overhead view of the same cluster
Base | Prob. Wrong
T | <1%
Output
T
T
T
A
A
A
A
<1%
A
A
A
T
T
T
T
<1%
T
T
T
G
G
C
G
30%

## Slide 8: Illumina Output: Fastq Format
Sequencing-By-Synthesis
Single Cluster
Base | Prob. | Phred Score | Code
T | 0.01% | 40 | H
A | 0.1% | 30 | ?
T | 0.05% | 33 | B
G | 30% | 5 | &
A | 1% | 20 | 4
C | 5% | 13 | .
Phred Score (Q) =
-log10(Prob. of Error)
Code comes from a subset of ASCII characters
**Note that different versions of Illumina use slightly different sets of codes
@Seqname:Flowcell:Lane:X1:Y1
TATGAC
+Seqname:Flowcell:Lane:X1:Y1
H?B&4.
@Seqname:Flowcell:Lane:X2:Y2
AAAGGG
+Seqname:Flowcell:Lane:X2:Y2
HH??AB
Fastq format (.fq or .fastq):
A text file with 4 lines per sequence

## Slide 9: Data Processing Pipeline
Raw Data
Cleaned Data
Aligned Reads
SNPs
Quality Check
Trimming
Remove leftover adapters
Map to Reference
Sort mapped reads
Merge aligned reads for all individuals
Find any site different b/t at least 2 samples
FASTQ
FASTQ
SAM/BAM
VCF
Minimum quality to “trust” a base call
Minimum length to keep a trimmed read
How many mismatches to allow
Coverage req. to call a SNP w/in a sample
Min. mapping quality to trust a read
# Samples required to keep SNP

## Slide 10: Read Mapping/Alignment
Reference Genome:
1
3
4
2
Some reads from a .fq file:
Read ID | Mapped Pos. | Mapping Qual. | CIGAR string
1
1
3553
37
100M
5
2
2
2041
37
5M1I9M3D85M
3
3
3
3998
10
100M
4
4
4
114
0
100M
5
*
*
*
Real SAM format has 11 fields or more (https://genome.sph.umich.edu/wiki/SAM)
Default SAM: 1 line per alignment, BUT
Default BWA/Bowtie: 1 line per read, with best alignment

## Slide 11: SNP Calling
Reference Genome:
Map. Rds
Sample 1:
Map. Rds
Sample 2:
Coverage too sparse
Typical Default: 10X cov
Missing 1 sample completely
SNP Pos | Ref | Alt | Qual | Format | Sample 1 | Sample 2
1055 | T | G | 30 | GT:DP:AD:GQ | 1/1:3:0,3:37 | 0/0:3:3,0:23
2113 | G | T | 20 | GT:DP:AD:GQ | 0/0:3:3,0:37 | 1/1:3:0,3:16
4678 | T | C | 33 | GT:DP:AD:GQ | 0/0:3:3,0:22 | 0/1:4:1,3:35
8327 | A | C | 16 | GT:DP:AD:GQ | 0/1:4:1,3:12 | 0/0:3:3,0:18
Full VCF details:
https://en.wikipedia.org/wiki/Variant_Call_Format
Type of quality value will depend on SNP calling program used
Vcftools (http://vcftools.sourceforge.net/) is a useful suite of programs for filtering and manipulating vcf files after calling SNPs